## Slide 1: SCBA/PPE Refresher & RIT CPR

## Slide 2: Objectives
1. Identify and describe the safety requirements when using the SCBA/PPE.
2. Describe the differences in the Township SCBA SOG and the generic guidelines.
3. Describe the safety rules when wearing the SCBA
4. Demonstrate the donning and doffing of the SCBA while wearing protective clothing.

## Slide 3: Materials Needed For This Lesson
Structural firefighting turnout gear, including gloves and hood.
Self-Contained Breathing Apparatus (SCBA)
Township Fire SOG 2-1-6
Township Fire SOG 2-1-7
Fundamentals of Firefighter Skills and Hazardous Materials Response, Fourth Edition

## Slide 4: SCBA/PPE Safety
1. Why do we wear SCBA and Personal Protective Equipment?
  PPE is designed to protect against a limited amount of heat.
    Different PPE for different activities
      Structural
      Wildland
      Haz Mat
      EMS
  Protect our lungs from airborne contaminants and carcinogens.
  Maintain breathing air in IDLH environments.

## Slide 5: SCBA/PPE Safety con’t.
How Does Structural PPE protect us?
  Provides thermal protection.
  Repels water
  Provides impact protection
  Protects against cuts and abrasions
  Furnishes padding against injury
  Provides respiratory protection

## Slide 6: SCBA/PPE Safety con’t.
Why that helmet?
  Provides thermal protection.
  Protects the head from falling debris and the ears with the included flaps.
  Deflects water away from the head and neck.
  Provides impact protection, outer shell, in conjunction with the inner suspension liner protects against falling objects
  Usually has one type of built-in or external eye protection.

## Slide 7: SCBA/PPE Safety con’t.
Protective hood
  Provides thermal protection for head and neck when head is turned, or neck is flexed.
  Constructed of Nomex, PBI or carbon fiber.
  Hoods are worn over the SCBA facepiece but under the helmet.
  Hood must fit snugly around the clear area of the facepiece so vision is not compromised, and hot gases cannot leak between the facepiece and hood.

## Slide 8: SCBA/PPE Safety con’t.
Turnout Coats and Pants
  Constructed of three layers; Nomex/PBI outer shell, a moisture barrier which is attached to the inner thermal barrier.
  The moisture barrier prevents the transfer of steam, water and other fluids to the skin. The barrier is critical as it protects against superheated steam which is created when large amounts of water is applied to fire thereby engulfing firefighters and burn unprotected skin.
  Coats come in two sizes, long and short and must be matched to the correct turnout pants to ensure that the midsection is covered if the firefighter raises their arms over their head.

## Slide 9: SCBA/PPE Safety con’t.
Limitations
  To provide protection, each component must be properly donned and correctly secured.
  The ensemble is not easy to don.
  Donning takes practice to be able to do it quickly and correctly.
  PPE is heavy and can add 50lbs of additional weight.
  As well as keeping moisture out, PPE keeps moisture in making it difficult for the body to cool itself.
  Senses are dulled wearing heavy gloves, facepieces and turnout gear.

## Slide 10: Donning PPE
Putting on protective clothing must be done in a specific order.
Following a set pattern of donning reduces the amount of time it takes.
Prepare your equipment for donning
  Place the legs of your pants over the boots and fold the pants down around them.
  Place your hood on top of your pants to remind you to put on your hood.
  Layout or hang your coat, gloves and helmet.

## Slide 11: Donning PPE con’t.
Recommended Steps
  Place your hood on your head and down around your neck.
  Step into your boots, pull up your pants. Place the suspenders over your shoulders and secure the front of the pants.
  Put on your coat and secure the inner and outer closures.
  Place your helmet on your head and pull the ear flaps down and secure the chinstrap.
  Turn up your collar and secure it in the front.
  Put on your gloves.
  Check all clothing to be sure it’s properly secured and have your partner check your clothing as well.

## Slide 12: SCBA Pre-Check
Check the air cylinder gauge to ensure that it is full. National Fire Protection Association (NFPA) 1404: Standard for Fire Service Respiratory Protection Training. NFPA 1404 Standard recommends that a minimum of 90% of the cylinder’s rated capacity is a full cylinder. Check cylinder pressure gauge for full indication. If indicated cylinder pressure is below 4000 psi, replace with a fully charged cylinder. (Township Fire SOG 2-1-6) Check the latest cylinder hydrostatic test date to ensure it is current. (Within three (3) years for composite lightweight cylinders.)(Township Fire SOG 2-1-6)

## Slide 13: SCBA Pre-Check con’t.
Check the remote gauge and the cylinder gauge Ensure that the gauges read within 100 psi of the same pressure. Ensure that gauges not marked in increments of 100 psi are the same Check the harness assembly and the face piece to ensure that all the straps are fully extended. Operate all the valves. Ensure that they operate properly. Ensure that they are in the correct position. Check the personal alert safety system (PASS) device manually for proper operation.

## Slide 14: Practice Time!!
Focus on doing it right, then doing it quickly. Putting your gear on quickly but improperly is as dangerous as it is time consuming to re-equip. Not wearing your PPE/SCBA correctly can cost YOU or your fellow firefighters, their LIVES! Practice how you play. Only through repetition will it become second nature.

## Slide 15: Firefighter Down CPR Ten Step Process

## Slide 16: Objectives
Initiate immediate CPR on a firefighter in full Turnout Gear with an SCBA that suffered a sudden cardiac arrest
Remove firefighter from the Turnout Gear and SCBA without interrupting compressions

## Slide 17: Step 1
Rescuer 1
Position downed Firefighter’s SCBA
between legs
Notes: Step 1:
  Rescuer 1: Drag the downed firefighter to a safe location to initiate care.
  Rescuer 1 should drag the firefighter from behind, drop to the ground and position the SCBA bottle between Rescuer 1 legs.
  Rescuer 1 legs will serve to stabilize the SCBA so that it can be used as CPR platform.

## Slide 18: Step 2
Rescuer 2
Pop open chest clip (if equipped) and begin
high quality compressions
Notes: Step 2:
  Rescuer 2: Should pop open the chest clip of the SCBA if applicable and initiated high quality compressions thru the Turnout Gear Jacket.
  Rescuer 2 should be a firefighter a “fresh” firefighter, (i.e. the engineer or a member of RIT that has not yet performed strenuous firefighting activity).
  The quality of compressions are paramount, and under this circumstance, fatigue and a decline in compression quality will be rapid.

## Slide 19: Step 3
Rescuer 1
Open SCBA bypass valve
Notes: Step 3:
  Rescuer 1: If the SCBA mask is still in place, open the SCBA bypass valve. This step can also be performed by Rescuer 2 quickly.
  The purpose of this is two-fold:
    to allow for passive ventilation with compressions, and
    allow for rescuers to identify an etiology of cardiac arrest. We can identify if the down firefighter ran out of air and address aggressive oxygenation. The SCBA air level gages should be inspected following removal of the down firefighter.

## Slide 20: Step 4-8
Step 4 – 8 should be performed in a coordinated method but simultaneously to the best of the ability of the rescuers
Do not interfere with compressions
Do not interrupt compressions
Depending on the style of gear your department carries, modifications may need to be made
You are firefighters - get the job done!

## Slide 21: Step 4
Rescuer 1
Remove helmet, mask, and hood

## Slide 22: Step 5
Rescuer 3
Start unbuckling the TOG jacket
from the bottom up
Notes: “TOG” is “Turnout Gear”

## Slide 23: Step 6
Rescuer 1
Loosen shoulder straps and position arms above the head

## Slide 24: Step 7
Rescuer 1 and Rescuer 3
Work closures and jacket open, do NOT
interfere with chest compressions

## Slide 25: Step 8
Rescuer 1
Hold the jacket and SCBA straps,
prepare for “PULL DOWN”
Notes: Step 8:
  Rescuer 1: (This is a make or break step.) Rescuer 1 needs to grasp the turnout gear jacket and the SCBA shoulder straps of the down firefighter firmly. Prepare for the “pull down.” Rescuer 1, who is at the head of the down firefighter, will give the final command to perform the “pull down.”

## Slide 26: Step 9
Rescuer 3 and Rescuer 4
Perform “PULL DOWN” by grabbing one leg each and pulling the victim out of their gear
Notes: Step 9:
  Rescuer 3 and Rescuer 4: Each Rescuer needs to firmly grab one of the down firefighter legs and coordinate the “pull down” method with Rescuer 1 at the head. Rescuer 1 will give the command to perform “pull down.” Rescuer 3 and Rescuer 4 will pull the down firefighter toward his/her feet and out of the turnout gear jacket and SCBA.

## Slide 27: Step 10
All Rescuers
Initiate comprehensive
Resuscitation Bundle!
Notes: Step 10:
  All rescuers: Initiate a comprehensive resuscitation bundle!
  The first step is to continue high quality compressions with a “fresh” person.
  Pulse checks may be considered at this time.

## Slide 28: See it in Action
https://www.youtube.com/watch?v=SeNZnm_ayiA&list=PLp3fuoGv1jSMebNNvIoemNv8fG7ukJStE&index=3
Notes: Step 10:
  All rescuers: Initiate a comprehensive resuscitation bundle!
  The first step is to continue high quality compressions with a “fresh” person.
  Pulse checks may be considered at this time.